I-stair Brochure

I-stairs patent info

# Text boxes

Safety Bulletin

These photos are of a new type of stair assembly that is being built into new residential construction. Instead of using 2” x 12” lumber for the stringers on the side and middle, it uses a 2” x 4” board, only on the edges. The steps and risers are ¾ inch OSB. The triangles holding the steps are light weight steel and attached to the 2” x 4”s by glue and nails. According to the designer of the system, the system would be protected by drywall if the unit is going from the main floor to the upstairs. However, from the basement to the main floor, in an unfinished area, drywall is not required. The metal shown on the bottom of the stair tread is similar to a gusset plate on manufactured trusses.